## Slide 1
Youngchul choi
Master’s Student in Coastal Hazards Lab at The University of Texas at Austin
Jan 5 2026
How to Run ClaymoreUW Remotely
ClaymoreUW using Material Point Method
: Running Sample simulation
Notes: Today, I’d like to give you a quick introduction to ClaymoreUW, the tsunami modeling tool I’ve been using. I’ll walk you through what it is and show you how to run a sample simulation using it.

## Slide 2: Process – Remote run
Clone the Git Repository
Build & Compilation
Run the program (Test simulations)
Run multiple simulations

## Slide 3: Process 1: Clone the Git Repository
Open editor & terminal VS code
  Connect SSH to Lonestar6(LS6.TACC.UTEXAS.EDU)
  Open bash terminal
Go to root directory to clone ClaymoreUW
  cd /scratch/10077/ycchoi1313/
  git clone https://github.com/youngdie07/claymore.git folder_name
Change the GPUs compute capability architecture (gpu-a100)
  setup_cuda.cmake
    set(TARGET_CUDA_ARCH -arch=sm_80)
    set(CMAKE_CUDA_ARCHITECTURES 80)
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 4: Process 2: Build / Compile
Set modules (GCC/NVCC)
  module load cuda/12.2
  module load gcc/12.2.0
Build
  cd claymore
  mkdir build
  cd build
  cmake ..
  cmake --build .
Adjust Setting.h – please refer to ‘How to adjust parameters’ file
Compilation
  cd ..
  sh local_build.sh
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 5: Process 3: Run the program
Get GPU-A100 allocation (submitting sbatch)
  Connect ssh c000-000(gpu ID) in bash or tmux
Check specs
  nvidia-smi
    ex) NVIDIA A100-PCIE-40GB
  module list
    module avail cuda
      ex) cuda_12.0
    module avail gcc
      ex) gcc (Ubuntu 10.5.0-1ubuntu1~22.04) 10.5.0
  Set cuda, gcc version
    module load cuda/12.2
    module load gcc/12.2.0
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 6: Process 3: Run the program
Move to OSU_LWF directory
  cd /scratch/10077/ycchoi1313/claymore/Projects/OSU_LWF/
  Two sample JSON input file
    scene.json
    scene_OSU-LWF_Mascarenas2022_BreakingWave_2D_1GPU_2024.10.23.json
Run the code
  ./osu_lwf --file=scene.json
  ./osu_lwf -f ./scene_OSU-LWF_Mascarenas2022_BreakingWave_2D_1GPU_2024.10.23.json
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 7: Process 4: Run multiple simulations
Customizing the .sh file: refer to the file available in the Github repository for guidance
  Module load
    module load cuda/12.2
    module load gcc/12.2.0
  GPU logging
    Regularly monitor GPU usage to detect the memory errors during simulations
  Forcing number of GPUs
    Set CUDA_VISIBLE_DEVICES=0,1,2 (Specific to Lonestar6, which has 3 GPUs).
    This prevents unnecessary memory issues caused by mismatched GPUs counts
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 8: References and Resources
https://docs.tacc.utexas.edu/hpc/lonestar6/