## Slide 1
Youngchul choi
Master’s Student in Coastal Hazards Lab at The University of Texas at Austin
mar 28 2025
Program
Basic tutorial
ClaymoreUW using Material Point Method
: Running Sample simulation
Notes: Today, I’d like to give you a quick introduction to ClaymoreUW, the tsunami modeling tool I’ve been using. I’ll walk you through what it is and show you how to run a sample simulation using it.

## Slide 2: What is ClaymoreUW
Claymore(Wang et al., 2020b)
  A numerical method based on the Material Point Method (MPM) for simulating the physical behaviors of materials undergoing:
    Multi Phase / Material,
    Large deformation & Self collision
ClaymoreUW(Bonus, 2023)
  A rebuilt version of Claymore by a research group at the University of Washington to increase accessibility and viability for engineers
  One of the tsunami event tools used in HydroUQ(Simcenter S/W)
Material Point Method (MPM)
  a hybrid Euler-Lagrangian numerical method that is best suited for modeling history-dependent materials in a dynamic, large deformation setting
    Material bodies are discretized by points(particles), which hold positions and deformation gradients (Lagrangian scheme)
    Space is discretized by a grid, where grid-nodes hold momentum (Eulerian scheme)
Notes: So, what exactly is ClaymoreUW?
ClaymoreUW is a rebuilt version of the original Claymore program developed by Wang et al. It was redesigned by a research group at the University of Washington to make it more accessible for engineering use.
It’s based on the Material Point Method (MPM), which is a hybrid method that combines grid-based and particle-based calculations. This makes it much better suited than traditional CFD models for simulating things like tsunami debris impact or landslides, where you have multi-phase and multi-material interactions.
In this method, materials like water or debris are represented by particles (or points), which carry their positions and deformation gradients. Boundaries—like the ground, walls, or structures—are represented on a grid. The nodes in the grid calculate things like momentum, velocity, or force based on the nearby particles. So overall, MPM is more flexible and better for modeling complex interactions and deformation compared to traditional models.

## Slide 3: Pre-Requirement
Local run
  Windows Subsystem for Linux(WSL2)
  https://learn.microsoft.com/en-us/windows/wsl/install
Remote run
  TACC allocation, other ssh tools (e.g. Filezilla)
  https://tacc.utexas.edu/
Code editing & debugging
  Visual Studio Code(VS Code) is recommended
  https://code.visualstudio.com/download
3D Visualization S/W
  Houdini Apprentice
  https://www.sidefx.com/products/houdini-apprentice/
Notes: To run a simulation, there are a few things you’ll need to install first.
Today, I’ll mainly show you how to run a sample simulation on my laptop. But if you're working with a larger domain or coarser resolution, you'll eventually need to use a supercomputer.
Since ClaymoreUW is Linux-based, if you want to run it locally on Windows, you’ll need to install WSL2. You can easily find it using the link here.
If you plan to use UT’s supercomputer, you’ll need a TACC account and an allocation—you can get help by discussing that with Dr.Lee. Also, you’ll need an SSH-based file manager, which Hyunje mentioned in his HPC seminar last fall.
For editing code, I highly recommend using VS Code. It’s super convenient because you can directly connect to your SSH environment and edit files on the remote system.
Lastly, one of the key outputs from this simulation is a 3D file in .bgeo format. To view it, you’ll need to download Houdini Apprentice, which is a free version of the software used in the 3D animation industry. It takes a little time to get used to, but I’ll just show you the basics today.

## Slide 4: Process
Clone the Git Repository
Adjust Settings
Build / Local Compilation
Run the Program
Check Output
Notes: Here’s how the tutorial will go: First, we’ll clone the ClaymoreUW GitHub repository, set up the simulation environment, and compile it locally. The compilation usually takes about over 30 minutes, so while that’s happening, I’ll explain how to set input parameters—things like wave types, bathymetry, debris, sensors, and forest structures—and then run a sample simulation. We’ll also take a quick look at the output.

## Slide 5: Clone the Git Repository
Open editor & terminal in VS code
  Go to root directory to clone ClaymoreUW
In terminal(wsl), enter:
  git clone https://github.com/youngdie07/claymore.git claymore-test
Change the corresponding GPUs compute capability architecture
  vim setup_cuda.cmake
    set(TARGET_CUDA_ARCH -arch=sm_89)
    set(CMAKE_CUDA_ARCHITECTURES 89)
Check specs
  nvidia-smi
    ex) NVIDIA RTX 2000 Ada Generation
  nvcc --version
    ex) cuda_12.0
    sudo apt-get install cuda-12-0
  gcc --version
    ex) gcc (Ubuntu 10.5.0-1ubuntu1~22.04) 10.5.0
    sudo update-alternatives --install /usr/bin/gcc gcc /usr/bin/gcc-9 10
Notes: Let’s open the terminal in VS Code, go into WSL, and clone the GitHub repository. This will copy all the necessary program files into your WSL folder.
But to actually run the program, you need to compile it locally.
Before you compile, make sure to edit your .cmake file depending on your GPU setup, and check that your nvcc and gcc versions are compatible—otherwise, you’ll get build errors at the next step.

## Slide 6: Clone the Git Repository
Internet Connection Issue (in WSL2)
  Debug with ping google.com
  Connect internet by
    sudo nano /etc/resolv.conf
    nameserver 8.8.8.8
    nameserver 8.8.4.4
Issues with CUDA, GCC, NVCC, or dependencies
  Depending on your GPU
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 7: Build / Local Compilation
Build
  cd claymore
    mkdir build
    cd build
    cmake ..
    cmake --build .
Adjust Setting.h (for high resolution simulation)
  cd Projects/OSU_LWF/setting.h
    // * GPU set-up.
    constexpr int g_device_cnt = 1; //< IMPORTANT. Num. GPUs to compile for. Default 1.  3
    // * Grid set-up
    #define DOMAIN_BITS 11 //< Domain resolution. 8 -> (2^8)^3 grid-nodes. Increase = finer grids.  12
    // * Grids
    constexpr int g_max_active_block = 25000; //< Max active blocks in gridBlocks. Preallocated, can resize. Lower = less memory used.  200,000
    // * Particles
    constexpr int g_max_particle_num = 4000000; //< Max no. particles. Very important, affects memory usage and performance. Preallocated, can resize.  200,000,000
Local Compilation
  cd ..
  sh local_build.sh
Notes: Now, here’s how you build the program locally. Just follow the steps shown here—it usually takes more than 30 minutes, so I’ll skip this part.
But if you have question on this step, please reach out to me because it requires some trouble shooting depending on your gpu model.
One important thing: Before you run sh local_build.sh, go into Projects/OSU_LWF/setting.h and adjust the simulation settings as needed. For example, if you want to use multiple GPUs or run a high-resolution simulation with 2.5 cm grid size, you’ll need to set that up here before compiling, so the changes are actually applied.
여기서 못기다리니까, ClaymoreUW_Tutorial/my-claymore 폴더가서
바로 JSON 파일 설명

## Slide 8: Run the program
Move to OSU_LWF directory
  cd Projects/OSU_LWF
  Two sample JSON input file
    scene.json
    scene_OSU-LWF_Mascarenas2022_BreakingWave_2D_1GPU_2024.10.23.json
Run the code
  ./osu_lwf --file=scene.json
Check the simulation Log
  The number of particles
    Scene.json : (total) 1,262,920 < g_max_particle_num = 4,000,000
    Scene_OSU-LWF ~.json: (total) 608,001
  The number of block
    Scene.json : (total) 12,222 (4074 per model) < Max blocks 25,000
    Scene_OSU-LWF ~.json: (total) 1,651
Notes: Once, let’s say, we finish the compiling and everything’s set, you’re ready to run the simulation.
So basically the input file of this simulation is JSON format.
Inside the Projects/OSU_LWF folder, you’ll find two scene files:
scene.json, which is a simple sample script, and
scene_OSU-LWF~.json, a thin-slice digital twin of the Oregon State University Large Wave Flume.
Today, we’ll run the OSU_LWF scene to get a better understanding of the input parameters.
And if we have time, I’ll show you how I run the forest model on the supercomputer.
So let’s start by running the OSU_LWF sample model.
It’s running now…
In the meantime, let’s look at how the input file looks like.

## Slide 9: Run the program
Key Parameters Overview (Bonus, 2023 – 4.8 ClaymoreUW User Guide; p76)
  "simulation": { }
  "models": [{ }]
    "device": {...},
    "material": {...},
    "algorithm": {...},
    "geometry": [{...}, ...],
    "output": {...},
  "grid-boundaries": [{...}, ...],
  "grid-sensors": [{...}, ...],
  "particle-sensors": [{...}, ...]
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 10: Run the program
Key Parameters Overview (Bonus, 2023 – 4.8 ClaymoreUW User Guide; p76)
  "simulation": { } - grid size, time-step, duration, frame per second, etc.
  "models": [{ }] - fluid, solid box, etc.
    "device": {...},
    "material": {...},
    "algorithm": {...},
    "geometry": [{...}, ...],
    "output": {...},
  "grid-boundaries": [{...}, ...], - wall, bathymetry, structure
  "grid-sensors": [{...}, ...], - velocity, force, etc.
  "particle-sensors": [{...}, ...] - water level, location etc.
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 11: Run the program
Key Parameters Overview - simulation
"simulation": {
"gravity": [0.0, -9.80665, 0.0],
"fps": 10,
"frames": 320,
"time": 0,
"default_dt": 0.5e-4,
"default_dx": 0.05,
"domain": [90, 4.5, 3.65],
"save_suffix": ".bgeo",
"particles_output_exterior_only": false,
"froude_scaling": 1.0
},
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 12: Run the program
Key Parameters Overview – models – device / material
"bodies": [
{
"gpu": 0,
"model": 0,
"material": {
"type": "particles",
"constitutive": "JFluid",
"CFL": 0.425,
"rho": 998.0,
"bulk_modulus": 2.0e8,
"gamma": 7.125,
"viscosity": 0.001
},
Notes: CFL number is a dimensionless parameter, typically between 0 and 1, that determines the stability of the numerical scheme
Bulk modulus : a measure of the ability of a substance to withstand changes in volume when under compression (2.2 Gpa)

## Slide 13: Run the program
Key Parameters Overview – models- algorithm
"bodies": [
{
"algorithm": {
"ppc": 8.0000,
"use_FEM": false,
"use_ASFLIP": false,
"use_FBAR": true,
"ASFLIP_alpha": 0.0,
"ASFLIP_beta_min": 0.0,
"ASFLIP_beta_max": 0.0,
"FBAR_psi": 0.98,
"FBAR_fused_kernel": true
},
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 14: Run the program
Key Parameters Overview – models – geometry (fluid)
"bodies": [
{
"geometry": [
{
"object": "OSU LWF",
"operation": "Add",
"span": [88.1, 1.85, 0.05],
"offset": [1.9, 0.0, 0.0],
"array": [1, 1, 1],
"spacing": [0.0, 0.0, 0.0],
}
],
Notes: It looks like the bathymetry coordinates are embedded in this file.

## Slide 15: Run the program
"bodies": [
  {
  "object": "Box",
  "operation": "Add",
  "span": [88.1, 1.75, 3.65],
  "offset": [1.9, 0.0, 0.0]
  },
  {
  "object": "Bathymetry",
  "operation": "Subtract",
  "use_custom_bathymetry": true,
  "domain_start": [0,0,0],
  "domain_end": [90, 4.5, 3.65],
  "bathymetry": [
  [0.0, 0.175],
  [19.70, 0.175],
  [23.35, 0.175],
  [34.35, 1.125],
  [49.00, 1.725],
  [74.60, 1.725],
  [89.45, 2.625],
  [90.00, 2.625]
  ]
  }
],
Key Parameters Overview – models – geometry(Custom)
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 16: Run the program
Key Parameters Overview – models – output
"bodies": [
{
"output_attribs": ["ID", "Pressure", "Velocity_X", "Velocity_Y"],
"track_attribs": ["Position_X"],
"target_attribs": ["Position_Y"],
"velocity": [0.0, 0.0, 0.0],
"track_particle_id": [0],
"partition_start": [0.0, 0.0, 0.0],
"partition_end": [89.1, 1.85, 0.05]
},
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 17: Run the program
Key Parameters Overview – grid boundaries
  "boundaries": [
  {
  "type": "grid",
  "object": "Wall",
  "contact": "Separable",
  "domain_start": [0.0, 0.0, 0.0],
  "domain_end": [90, 4.5, 0.05],
  "time": [0, 180]
  },
  {
  "type": "grid",
  "object": "OSU LWF",
  "contact": "Separable",
  "domain_start": [0.0, 0.0, 0.0],
  "domain_end": [90, 4.5, 0.05],
  "time": [0, 180]
  }
Notes: It looks like the bathymetry coordinates are embedded in this file.

## Slide 18: Run the program
Key Parameters Overview - grid-boundaries
  "boundaries": [
  {
  "type": "grid",
  "object": "Box",
  "contact": "Separable",
  "domain_start": [45.79, 2.1, 0.0],
  "domain_end": [46.86, 2.715, 1.016],
  "time": [0, 180]
  },
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 19: Run the program
Key Parameters Overview – grid-boundaries
  "boundaries": [
  {
  "type": "grid",
  "object": "OSU Paddle",
  "contact": "Separable",
  "domain_start": [1.6, -0.2, -0.2],
  "domain_end": [2.0, 5, 4],
  "time": [0, 180],
  "file": "wmdisp_hydro2sec_1200hz_smooth_14032023.csv",
  "output_frequency": 1200
  }
  ],
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 20: Run the program
Key Parameters Overview - grid-sensors
  "grid-sensors": [
  {
  "type": "grid",
  "attribute": "Force",
  "operation": "Sum",
  "direction": "X+",
  "output_frequency": 120,
  "domain_start": [45.790, 2.1, -0.2],
  "domain_end": [45.85, 2.615, 2.338]
  }
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 21: Run the program
Key Parameters Overview - particle-sensors
  "particle-sensors": [
  {
  "type": "particles",
  "attribute": "Elevation",
  "operation": "Max",
  "output_frequency": 120,
  "domain_start": [16.0, 1.0, 0.0],
  "domain_end": [16.1, 3.6, 1.0]
  }
  ]
  }
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 22: Check Output
OBJ files
  Domain
  Boundary
BGEO files
  Particles
  particleTarget
  gridTarget
CSV files
  Water level
  Velocity
  Load
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 23: Check Output
Tips for 3D Visualization in Houdini
  At the object panel: Tap and create ‘geometry’
  Inside the geometry, tap ‘file’ and import .obj and .bgeo files.
  You can check your 3D model.
  Some visualization tips:
    Visualization attribute: you can see color/mark of particle’s attributes (e.g. velocity or pressure)
    Some boundaries(box array or cylinder) are not automatically created from simulation output so you need to create those .obj files separately or transform&copy to make an array.
    You need to also create customized Bathymetry.obj by yourself (the sample code’s OSU-LWF bathymetry is offered in Github: https://github.com/JustinBonus/HydroUQ/blob/ 1a9b2dd557c5e72f8a06efd382e49644fe6e60de/OSU_LWF_Bathymetry.obj#L4
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 24: Clone the Git Repository – remote run
Open editor & terminal VS code
  Connect SSH to Lonestar6(LS6.TACC.UTEXAS.EDU)
  Open bash terminal
Go to root directory to clone ClaymoreUW
  cd /scratch/10077/ycchoi1313/
  git clone https://github.com/youngdie07/claymore.git folder_name
Change the GPUs compute capability architecture (gpu-a100)
  setup_cuda.cmake
    set(TARGET_CUDA_ARCH -arch=sm_80)
    set(CMAKE_CUDA_ARCHITECTURES 80)
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 25: Build / Compile – remote run
Set modules (GCC/NVCC)
  module load cuda/12.2
  module load gcc/12.2.0
Build
  cd claymore
  mkdir build
  cd build
  cmake ..
  cmake --build .
Adjust Setting.h
Local Compilation
  cd ..
  sh local_build.sh
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 26: Run the program – remote run
Get GPU-A100 allocation (submitting sbatch)
  Connect ssh c000-000(gpu ID) in bash or tmux
Check specs
  nvidia-smi
    ex) NVIDIA A100-PCIE-40GB
  module list
    module avail cuda
      ex) cuda_12.0
    module avail gcc
      ex) gcc (Ubuntu 10.5.0-1ubuntu1~22.04) 10.5.0
  Set cuda, gcc version
    module load cuda/12.2
    module load gcc/12.2.0
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 27: Run the program – remote run
Move to OSU_LWF directory
  cd /scratch/10077/ycchoi1313/claymore/Projects/OSU_LWF/
  Two sample JSON input file
    scene.json
    scene_OSU-LWF_Mascarenas2022_BreakingWave_2D_1GPU_2024.10.23.json
Run the code
  ./osu_lwf --file=scene.json
  ./osu_lwf -f ./scene_OSU-LWF_Mascarenas2022_BreakingWave_2D_1GPU_2024.10.23.json
Notes: # local build 방법 - window OS
- WSL2 설치/열기 (WSL 혹은 VS code)
0. 인터넷 연결
Sudo nano /etc/resolv.conf
Nameserver 8.8.8.8
Nameserver 8.8.4.4
Github에서 a local install of ClaymoreUW public repo:
cd ~
git clone https://github.com/youngdie07/claymore.git
(https://github.com/youngdie07/claymore/tree/master)
cd claymore
sudo apt install build-essential
nvidia-smi
- ex) NVIDIA GeForce RTX 4090
nvcc --version
- ex) cuda_12.0
gcc --version
- ex) gcc (Ubuntu 13.3.0-6ubuntu2~24.04) 13.3.0

## Slide 28: References and Resources
Github repository
  https://github.com/JustinBonus/claymore
  https://github.com/penn-graphics-research/claymore
Related Document
  https://claymore.readthedocs.io/en/latest/
  Bonus, J. (2023). Evaluation of fluid-driven debris impacts in a high-performance multi-GPU material point method (Order No. 30819170). Available from ProQuest Dissertations & Theses Global. (2915819774).